## Slide 1: TinyNPU: A Sensor-Driven Low-Latency AI Accelerator for Ballistic Vision
-Hariharan Ganesh

## Slide 2: Introduction & Problem Statement
The Challenge - Ballistic Vision: Tracking ultra-high-speed objects requires extremely low-latency object detection (YOLOv8n). - The Bottleneck: Traditional CPUs and GPUs have too much software overhead and memory latency. The Solution: - A custom, hardware-accelerated NPU deployed directly on the edge using a Zynq-7020 FPGA. - Fully deterministic, predictable latency running independent of an OS.

## Slide 3: TinyNPU Architecture Highlights
Core Engine: - 8x8 Systolic Array: Weight-stationary dataflow architecture maximizing MAC utilization. - INT8 Quantization: Replaces costly floating-point math with highly efficient 8-bit integer arithmetic. - Custom Activation: Features a 5-segment piecewise linear approximation for Sigmoid and ReLU to save BRAM. Data Movement: - AMBA AXI4 Standards: AXI4-Lite for configuration registers and AXI4-Stream for high-bandwidth DMA. - Double Buffering: Hides memory latency by pre-fetching weights and activations.

## Slide 4: Overcoming Edge Constraints
Depthwise Separable Convolution Optimization: - Heavily optimized our engine for Depthwise convolutions used in modern edge networks like YOLO. - DSP Optimization: Implemented a 2-stage adder tree to reduce DSP cascade depth, improving max clock frequency. Pipelined Requantization: - Built a custom 3-stage pipelined requantization unit to handle INT32 to INT8 down-scaling without breaking timing.

## Slide 5: Rigorous Verification Methodology
Approach: - 100% Verilog/SystemVerilog: No Python in the critical verification path to ensure ASIC-portability. - Hardware Scoreboard: Built a robust testbench that compares AXI-Stream outputs against a golden hex file bit-by-bit. Results: - Functional Accuracy: 100.00% detection accuracy verified over 4,096 bytes of simulated data. - Zero Errors: 0 false positives, 0 false negatives.

## Slide 6: FPGA Implementation & Timing Closure
Target: Xilinx PYNQ-Z2 (XC7Z020CLG400-1) The Challenge: - Pushing the silicon to its limits resulted in initial routing congestion and negative setup slack. - The Fix: Removed inferred latches in clock gating cells, heavily pipelined the requantization unit, and optimized adder trees. The Result: - Successfully closed Setup Timing with a Worst Negative Slack (WNS) of +0.052 ns. - Synthesized in Out-Of-Context (OOC) mode for flawless system-level integration.

## Slide 7: Conclusion & Next Steps
Project Achievements: - Designed, verified, and successfully synthesized a complete, ASIC-ready AI accelerator from scratch. - Met all strict timing and resource constraints for the Zynq-7020 FPGA. Next Steps (System Integration): - Block Design: Package the TinyNPU as Vivado IP and connect it to the Zynq ARM Processing System. - Software Overlay: Use PYNQ's Python environment to stream real image data from the ARM core to the NPU. - Live Ballistic Testing: Deploy the system with a high-speed camera for real-time tracking.