## Slide 1
NPU
FINAL YEAR PROJECT
TinyNPU
An ASIC-Ready INT8 Systolic AI Accelerator
Deterministic Edge Inference · Pure Hardware Architecture · Zero ARM Dependencies
117 mW
On-Chip Power
195 MHz
Achieved fMAX
100%
ASIC Readiness
Verilog-2001
RTL Standard

## Slide 2
Problem Identification & Relevance
Why does edge AI demand a purpose-built hardware accelerator?
⚠ The Technical Bottleneck
▸ GPU-class devices draw excessive power, causing thermal throttling under sustained high-FPS inference workloads — incompatible with strict SWaP constraints.
▸ Hybrid FPGA/SoC platforms offload control to ARM+Linux, introducing OS jitter and non-deterministic interrupt latency into real-time inference pipelines.
▸ Most academic NPU IP cores are heavily software-assisted, making them impossible to port directly to silicon for an ASIC tapeout without significant redesign.
✦ Why It Matters
▸ SWaP Constraints — Mission-critical edge platforms (drones, autonomous sensors) impose hard limits on Size, Weight, and Power. Heatsinks are not an option.
▸ Determinism — Any OS interrupt or bus contention can cause a missed detection frame in high-speed visual tracking applications.
▸ ASIC Scalability — A strictly pure-RTL architecture can be migrated directly from an FPGA prototype to a 7nm foundry tape-out with zero architectural changes.

## Slide 3
Objectives & Expected Outcomes
Technical goals and measurable success criteria for this project.
01
Systolic Array Design
Design an 8×8 Weight-Stationary Systolic Array optimized for INT8 quantized multiply-accumulate operations with 2-stage pipelining.
02
Processor-Less Architecture
Eliminate ALL CPU/ARM overhead by building a complete, self-sufficient verification chain entirely in pure RTL hardware logic.
03
Power Optimization
Apply Integrated Clock Gating (ICG) across all clock domains via Vivado's power_opt_design engine to minimize dynamic switching power.
04
Silicon Verification
Flash the compiled bitstream directly to FPGA and confirm functional pass/fail using dedicated hardware scoreboards and physical board LEDs.

## Slide 4
Proposed Methodology
A four-phase rigorous ASIC physical design and verification flow.
Phase 1
RTL Design
2-stage MAC pipeline, multi-stage requantization units. Verilog-2001 strict compliance.
Phase 2
HW Architecture
Pure hardware BRAM Sensor Emulator replaces ARM processor. AXI-Stream data path.
Phase 3
Power Synthesis
power_opt_design infers ICG cells. BRAM EN-pin gating. ExploreWithRemap strategy.
Phase 4
On-Silicon Test
Bitstream flashed to PYNQ-Z2. Physical button triggers emulator. LED PASS/FAIL output.
➤
➤
➤

## Slide 5
System Architecture — Data Flow
Option A: Processor-less execution. Full AXI-Stream data path in pure RTL.
BRAM Emulator
Sensor Input Hex Image Data
AXI-Stream Bus
32-bit TDATA TVALID / TREADY
Systolic Array 8×8 PE Grid
INT8 MAC 2-Stage Pipeline
Requant Unit
4-Stage Pipe INT32→INT8
HW Scoreboard
Golden Ref PASS / FAIL
→
→
→
→
Input Stage
Hardcoded hex vectors simulate MIPI CSI-2 camera feed at full 125 MHz clock speed.
Compute Core
Weight-stationary dataflow maximises data reuse, minimizing expensive SRAM read cycles.
Output Stage
Real-time compare logic drives physical board LEDs for instant Pass/Fail results.

## Slide 6
Physical Verification Results
Post-route implementation metrics — Xilinx Zynq xc7z020 silicon (Vivado 2025.1)
117
mW Total On-Chip Power
DYNAMIC POWER
Ice-cold operation. Zero thermal throttling. No heatsink required.
195
MHz Max Frequency (fMAX)
TIMING RESULT
Target: 100 MHz. Achieved: 195 MHz. WNS = -0.120 ns @ 200 MHz.
0
Synthesis Errors | 0 Latches
ASIC RTL QUALITY
Verilog-2001 strict. No combinational loops. No software dependencies.
SYNTHESIS RESOURCE UTILIZATION
2
DSP48 Cells
607
FF Registers
775
LUT Count
160
BRAM Blocks
Inferred (ICG)
Clock Gating Cells
< 1%
Route Util

## Slide 7
Processing Speed & Pipeline Latency
Deterministic clock-cycle accurate latency — zero OS jitter, zero software overhead.
5.13
ns Clock Period
@ 195 MHz fMAX
24
cycles Drain Latency
2-stage MAC + 4-stage Requant
+0.033
ns Final WNS (Timing MET)
Post-route timing closure achieved
100%
Routes Complete
0 failed nets. 0 node overlaps.
PIPELINE STAGE LATENCY BREAKDOWN
AXI-Stream Input
1 cycle
Activation Buffer Write
1 cycle
Systolic Array MAC Stage 1
1 cycle
Systolic Array MAC Stage 2
1 cycle
Requant 4-Stage Pipe
4 cycles
Output Scoreboard
1 cycle
Total end-to-end pipeline latency: ~9 clock cycles @195 MHz = ~46 ns | Deterministic. No OS jitter. No interrupt-driven delays.

## Slide 8
Timing Closure Journey
Systematic diagnosis and resolution of setup violations — from WNS -1.285 ns to +0.033 ns PASS.
-1.285 ns
Initial Build
ROOT CAUSE: 11 LUT levels in one combinational cycle inside frame_gen.v comparison logic. Critical path too long.
FIX: Pipelined the comparison into 2 register stages to break the long logic chain.
-0.602 ns
After RTL Fix
ROOT CAUSE: Routing introduced additional hold slack issues. Physical optimization had not been applied.
FIX: Ran AggressiveExplore phys_opt_design strategy to retime and restructure the placed netlist.
-0.176 ns
After phys_opt
ROOT CAUSE: Clock domain skew discovered: u_pooling (ICG gated clock, +3.35 ns delay) drives u_threshold_filter (ungated clock).
FIX: Changed threshold_filter to use clk_postproc — same domain, eliminating the inter-domain skew.
+0.033 ns
FINAL — MET
ROOT CAUSE: Vivado used cached old netlist. Directly patched .gen/ipshared/bd96/src/tinynpu_top.v to force resynthesis.
FIX: Timing closure achieved. WNS positive. All 472 endpoints passing. Hold slack 0.172 ns.
TIMING CLOSED | WNS = +0.033 ns | TNS = 0.000 ns | 2/472 endpoints resolved | Hold Slack = 0.172 ns | FPGA SILICON VERIFIED

## Slide 9
References & Future Scope
Academic grounding and planned architectural extensions.
REFERENCES
[1] Jouppi, N.P., et al. (2017). "In-Datacenter Performance Analysis of a Tensor Processing Unit." ISCA.
[2] Chen, Y., et al. (2016). "Eyeriss: An Energy-Efficient Reconfigurable Accelerator for Deep CNNs." IEEE JSSC.
[3] Du, Z., et al. (2015). "ShiDianNao: Shifting Vision Processing Closer to the Sensor." ISCA.
[4] Xilinx Inc. (2025). Vivado Design Suite User Guide: Power Analysis and Optimization. UG907.
[5] IEEE Std 1364-2001. IEEE Standard for Verilog Hardware Description Language.
FUTURE SCOPE
> JTAG-to-AXI Video Streaming — Inject stored video frame-by-frame directly into the NPU data path via JTAG debug cable, with zero software on the chip.
> SRAM Macro Migration — Replace FPGA BRAM primitives with TSMC/GlobalFoundries standard-cell SRAM macros to prepare the design for full ASIC tapeout.
> DVFS Control Logic — Implement dynamic voltage and frequency scaling FSMs for sub-50mW idle power states during between-frame blanking intervals.
> Depthwise Separable Conv — Extend the systolic array with a DW convolution engine lane for MobileNet/YOLOv8 nano-scale layer support.