## Slide 1
SAVEETHA ENGINEERING COLLEGE
Department of Electronics & Communication Engineering | Affiliated to Anna University | Approved by AICTE
19EC702 - Project Work Phase I | Zeroth Project Review
TinyNPU
A Sensor-Aware Reconfigurable AI Accelerator
for Ultra-High-Speed Ballistic Vision
Platform
PYNQ-Z2 (Zynq-7020)
Domain
AI Hardware / VLSI Design
Frontend
Python PYNQ API + DMA
Review Date: 05 August 2026 | Time: 1:00 PM - 3:00 PM
Panel Members: Dr. Srigitha S. Nath, Dr. M. Selvi, Dr. S. Praveen Kumar & team
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
1 / 7

## Slide 2
Problem Identification & Relevance
Slide 2 of 7
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
2 / 7
The Core Problem
- Standard pipelines transfer raw pixels to CPU/GPU over PCIe
- PCIe bottleneck + OS scheduling = 5 to 50 ms latency overhead
- Ballistic threats travel > 300 m/s - every millisecond is critical
- Total sensor-to-decision budget: < 500 microseconds
- No existing solution co-locates sensor stream + CNN inference on-chip
Why Standard Solutions Fall Short
- GPU: High throughput but highly non-deterministic latency
- CPU: Too slow for real-time inference on live pixel streams
- Cloud NPU / TPU: High-bandwidth PCIe or network still required
- Edge MCUs: Insufficient compute for multi-layer CNN inference
Real-World Relevance
- Aerospace: Intercept micro-projectiles in < 1 ms
- Automotive: Sub-1 ms collision hazard detection at high speed
- Industrial: High-speed conveyor object sorting at > 100 fps
- Defense: Counter-drone and ballistic tracking systems
- Medical: High-speed surgical instrument real-time tracking
TinyNPU - Proposed Solution
- Near-sensor coprocessor on PYNQ-Z2 (Zynq-7020) board
- Python PYNQ API feeds sensor data via AXI4-Stream DMA
- 8x8 Weight-Stationary Systolic Array: 64 MACs per cycle
- INT8 quantized CNN layers: low memory and low power
- Target: single-digit microsecond end-to-end inference latency

## Slide 3
Objectives & Expected Outcomes
Slide 3 of 7
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
3 / 7
O1
Ultra-Low Latency
Achieve single-digit microsecond inference for Conv and Fully Connected layers on PYNQ-Z2
O2
Deterministic Execution
No caches or branch predictors - ensure strict cycle-level timing on FPGA fabric
O3
Resource Efficiency
Maximize Zynq-7020 DSP48E1 and BRAM utilization within tight FPGA resource budget
O4
ASIC Migration Readiness
100% vendor-neutral synthesizable Verilog RTL portable to any silicon process node
EXPECTED OUTCOMES
25.6 GOPS @ 200 MHz
< 10 us inference
INT8 / INT32 pipeline
AXI4 Interfaces
Python + FPGA Integrated

## Slide 4
PYNQ-Z2 Hardware Platform & Python Data Frontend
Slide 4 of 7
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
4 / 7
PYNQ-Z2 Board Specs
SoC
Xilinx Zynq-7020
FPGA Fabric
Artix-7 28nm PL
Processor
Dual ARM Cortex-A9 @ 667 MHz
DSPs
220 x DSP48E1 Slices
BRAM
140 x 36Kb Blocks
LUTs
53,200 Look-Up Tables
Memory
512 MB DDR3 SDRAM
Camera I/O
USB UVC Camera (OpenCV)
OS
Linux + Jupyter Notebook
Framework
PYNQ 3.x Overlay API
Python Sensor Data Pipeline
1
Step 1 - Load Overlay
from pynq import Overlay ol = Overlay('tinynpu.bit')
2
Step 2 - Init DMA + Camera
dma = ol.axi_dma cam = cv2.VideoCapture(0)
3
Step 3 - Capture & Quantize
_, frame = cam.read() quant = quant_int8(frame, scale)
4
Step 4 - Allocate & DMA Send
ibuf = allocate((H,W), 'i1') ibuf[:] = quant dma.sendchannel.transfer(ibuf)
5
Step 5 - Trigger & Read Back
dma.sendchannel.wait() dma.recvchannel.transfer(obuf) result = np.array(obuf)
Zynq PS-PL Integration
PROCESSING SYSTEM (PS)
- ARM Cortex-A9 Dual-Core
- Linux OS + PYNQ 3.x
- Python / Jupyter Frontend
- 512 MB DDR3 Buffer
AXI4-S DMA + HP0
PROGRAMMABLE LOGIC (PL)
- TinyNPU Overlay (.bit file)
- 8x8 Systolic MAC Grid
- AXI4-Lite CSR Register File
- AXI4-Stream Sink + Source
- Requant + ReLU + Pooling

## Slide 5
Proposed Methodology - TinyNPU Pipeline
Slide 5 of 7
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
5 / 7
1
Camera / Sensor Input
USB UVC Camera captured via OpenCV on PS
Pixel Frames
2
Python PYNQ Frontend
Overlay load, INT8 quantise, allocate DMA buffer
INT8 Buffer
3
AXI4-Stream DMA Transfer
HP0 high-perf port - frame sent to FPGA PL fabric
DMA Burst
4
TinyNPU Systolic Core
8x8 Weight-Stationary Grid | 64 INT8 MACs / cycle
INT32 Psums
5
Post-Processing Chain
Requant (INT32->INT8) + ReLU + 2x2 Max Pool
INT8 Activations
6
Result Output via AXI4-S
DMA recv on PS | Python processes prediction result
KEY DESIGN DECISIONS
Weight-Stationary Dataflow
- Filter weights stay static in PEs
- Activations stream across the grid
- Minimises weight read energy cost
Python PYNQ DMA Frontend
- Overlay API loads .bit to FPGA PL
- allocate() for contiguous DMA buf
- sendchannel.transfer() - zero copy
Double-Buffered Memory
- Ping-pong BRAM banks hide latency
- Sensor feeds Bank A while NPU
- processes Bank B simultaneously
Fixed-Point Requantisation
- INT32 -> INT8 via M0 x 2^(-n)
- 3-stage: bias add, scale mul, ASR
- Clamp to [-128, 127] at output
Single Clock Domain
- All blocks share one system clock
- No CDC synchronizers required
- Simplifies STA timing closure
AXI4 Bus Architecture
- AXI4-Lite: CSR config registers
- AXI4-Stream: activation/result I/O
- AXI4-DMA: weight prefetch engine

## Slide 6
System Architecture Overview
Slide 6 of 7
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
6 / 7
Python PYNQ Frontend (PS)
Overlay + DMA
AXI4-Lite Slave (CSR Registers)
Config & Control
AXI4-Stream Sink
Activation Input
DMA Controller
Weight Prefetch (AXI4 Master)
NPU Controller FSM
Load->Compute->Drain
Activation Buffer
256x64 Ping-Pong Dual BRAM
Weight Buffer
1024x64 Dual Port BRAM
DW Line Buffer
3x3 Depthwise Conv Engine
Output Buffer (FIFO)
Decouples NPU from host BW
Systolic Array - 8x8 MAC Grid
64 Processing Elements | INT8 x INT8 -> INT32 | Weight-Stationary Dataflow | 1 MAC / PE / cycle
64 DSP48E1 blocks | Skewed activation input | Deskewed INT32 psum output
Requantisation Unit
Bias+M0 Scale +ASR+Clamp
Activation Unit
ReLU / LeakyReLU / Bypass
Pooling Unit
2x2 Max / Avg / Bypass
AXI4-Stream Source
Output Result Stream
Interrupt Controller
Done flag to PS
Python Result Handler (PS)
DMA recv + prediction callback

## Slide 7
References
Slide 7 of 7
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
7 / 7
[1]
H. Kung & C. Leiserson
"Systolic Arrays for VLSI"
Sparse Matrix Proc., 1978
[2]
B. Jacob et al.
"Quantization and Training of Neural Networks for Efficient Integer-Arithmetic-Only Inference"
CVPR 2018
[3]
N. P. Jouppi et al.
"In-Datacenter Performance Analysis of a Tensor Processing Unit"
ISCA 2017
[4]
K. He et al.
"Deep Residual Learning for Image Recognition"
CVPR 2016
[5]
A. G. Howard et al.
"MobileNets: Efficient Convolutional Neural Networks for Mobile Vision"
arXiv:1704.04861, 2017
[6]
Xilinx / AMD
PYNQ-Z2 Reference Manual & Zynq-7020 Technical Reference Manual
UG585, 2023
[7]
ARM Ltd.
AMBA AXI4 and ACE Protocol Specification
IHI0022H, 2022
[8]
Y. Chen et al.
"Eyeriss: A Spatial Architecture for Energy-Efficient Dataflow for CNNs"
ISCA 2016