## Slide 1
SAVEETHA ENGINEERING COLLEGE
Department of Electronics & Communication Engineering | Affiliated to Anna University | Approved by AICTE
19EC702 - Project Work Phase I | Zeroth Project Review
TinyNPU
TinyNPU: A Sensor-Driven Low-Latency AI Accelerator for Ballistic Vision
Platform
PYNQ-Z2 (Zynq-7020)
Domain
AI Hardware / VLSI Design
Frontend
Python PYNQ API + DMA
Review Date: 05 August 2026 | Time: 1:00 PM - 3:00 PM
Panel: Dr. Srigitha S. Nath, Dr. M. Selvi, Dr. S. Praveen Kumar & team
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
1 / 7

## Slide 2
Problem Identification & Relevance
Slide 2 of 7
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
2 / 7
The Core Problem
Standard pipelines relay raw pixels to CPU/GPU over PCIe
PCIe bottleneck + OS scheduling = 5 to 50 ms latency
Ballistic threats travel > 300 m/s - every ms matters
Total sensor-to-decision budget: under 500 microseconds
Why Standard Solutions Fail
GPU: High throughput but non-deterministic latency
CPU: Too slow for real-time CNN inference on live frames
Edge MCUs: Insufficient compute for multi-layer CNN
Cloud NPU/TPU: PCIe or network bandwidth still required
Real-World Relevance
Aerospace: Intercept micro-projectiles in under 1 ms
Automotive: Sub-1 ms collision hazard detection
Industrial: High-speed conveyor sorting at 100+ fps
Defense: Counter-drone and ballistic tracking systems
TinyNPU Proposed Solution
Near-sensor coprocessor on PYNQ-Z2 (Zynq-7020) board
Python PYNQ API feeds sensor data via AXI4-Stream DMA
8x8 Weight-Stationary Systolic Array: 64 MACs per cycle
Target: single-digit microsecond end-to-end latency

## Slide 3
Objectives & Expected Outcomes
Slide 3 of 7
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
3 / 7
O1
Ultra-Low Latency
Achieve single-digit microsecond inference latency for Conv and FC layers on PYNQ-Z2
O2
Deterministic Execution
No caches or branch predictors - strict cycle-level timing on the FPGA fabric
O3
Resource Efficiency
Maximize Zynq-7020 DSP48E1 blocks and BRAM utilization within tight resource budget
O4
ASIC Migration Readiness
100% vendor-neutral synthesizable Verilog RTL - portable to any silicon process node
EXPECTED OUTCOMES
25.6 GOPS @ 200 MHz
< 10 us inference
INT8 / INT32 pipeline
AXI4 standard interfaces
Python + FPGA integrated

## Slide 4
Proposed Methodology - TinyNPU Data Pipeline
Slide 5 of 7
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
5 / 7
1
Camera Sensor
USB UVC via OpenCV
Pixel Data
2
PYNQ Frontend
Overlay + DMA INT8 Quantise
INT8 Buffer
3
TinyNPU Core
8x8 Systolic 64 MACs/cycle
INT32 Psums
4
Post- Process
Requant+ReLU +MaxPool
INT8 Activations
5
Result Output
AXI4-S -> DMA -> Python CB
KEY DESIGN DECISIONS
Weight-Stationary Dataflow
Filter weights stay static inside PEs
Activations stream across the 8x8 grid
Minimises weight BRAM read energy
Python PYNQ DMA Frontend
PYNQ Overlay API loads .bit to FPGA PL
allocate() gives contiguous DMA buffer
sendchannel.transfer() = zero copy
Double-Buffered Memory
Ping-pong BRAMs hide weight reload latency
Sensor writes Bank A while NPU reads Bank B
Maximises systolic array throughput
INT8 Fixed-Point Requantisation
INT32 accum -> INT8 via M0 x 2^(-n) scale
3-stage: bias add, scale multiply, ASR
Clamped to [-128, 127] at output stage

## Slide 5
System Architecture Overview
Slide 6 of 7
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
6 / 7
Python PYNQ Frontend (PS)
Overlay + DMA
AXI4-Lite Slave (CSR File)
Config & Control
AXI4-Stream Sink
Activation Input
DMA Controller
Weight Prefetch (AXI4 Master)
NPU Controller FSM
Load->Compute->Drain
Activation Buffer
256x64 Ping-Pong BRAM
Weight Buffer
1024x64 Dual-Port BRAM
DW Line Buffer
3x3 Depthwise Conv Engine
Output Buffer (FIFO)
Decouples NPU from host BW
8x8 Systolic Array - MAC Grid
64 Processing Elements | INT8 x INT8 Multiply-Accumulate | INT32 partial sums
Weight-Stationary dataflow | Skewed activation input | 64 DSP48E1 blocks
Requantisation Unit
Bias+M0 Scale +ASR+Clamp
Activation Unit
ReLU / Bypass
Pooling Unit
2x2 Max / Avg / Bypass
AXI4-Stream Source
Output Result Stream
Interrupt Controller
Done flag to PS
Python Result Handler (PS)
DMA recv + prediction callback

## Slide 6
References
Slide 7 of 7
SAVEETHA ENGINEERING COLLEGE | Dept. of ECE | 19EC702 - Project Work Phase I
7 / 7
[1]
ARSLAN MUNIR
CPU-Accelerator Co-Scheduling for CNN Acceleration at the Edge
[2]
B. Jacob et al.
"Quantization and Training of NNs for Efficient Integer-Only Inference"
ieee2020
[3]
Dharun Kanna N
CNN Accelerator For Edge Inference
ICNGCS 2025
[4]
  K. He et al.
"Deep Residual Learning for Image Recognition"
CVPR 2016
[5]
[6]
Xilinx / AMD
PYNQ-Z2 Reference Manual + Zynq-7020 Technical Reference Manual
UG585, 2023
[7]
ARM Ltd.
AMBA AXI4 and ACE Protocol Specification
IHI0022H, 2022
[8]
Y. Chen et al.
"Eyeriss: A Spatial Architecture for Energy-Efficient Dataflow for CNNs"
ISCA 2016